## Slide 1: Demo 1: Flow
Daniil Svyatsky & J. David Moulton
Los Alamos National Laboratory

## Slide 2: Outline
Flow Modeling and Simulation with ATS
Flow is a critical driver in ecosystem dynamics
Variably saturated flow
  Richards’ Equation
  Infiltration in 1D column
Overland flow
  Diffusive Wave Equation
  Simple geometry, rainfall inducing flow, highlight different outflow boundary conditions
Integrated Hydrology
  Coupling of Surface/Subsurface flow
  Hillslope hydrology spinup simulation
  Hillslope irrigation simulation

## Slide 3: Motivation/Background

## Slide 4: Flow plays a critical role in driving and coupling processes
Climate impacts and feedbacks (carbon and nitrogen cycling).
Contaminant transport and reactions.
Complex interaction of land surface and subsurface processes.

## Slide 5: Subsurface Flow
Richards’ Equation

## Slide 6: Variably Saturated Flow: Richards’ Equation
Richards (1931) model for variably saturated flow
Φ - soil porosity [-]
nl - molar water density [mol m-3]
kr - relative permeability [-]
k - absolute permeability [m2]
μ - dynamic viscosity [Pa s]
ρ - mass water density [kg m-3]
g - gravity [m s-2]
where the unknowns are the water pressure p [Pa] and the Darcy flux q [mol m-2 s-1]

## Slide 7: Water Retention Models
Nonlinear models for kr(p) = k(s(p)) and for s(p) are defined by van Genuchten and Mualem equations:
where m, n=1/(1-m) and are parameters of the water retention model.

## Slide 8: Infiltration into a 1D soil column (Transient)
Initial condition
  Hydrostatic pressure with water table at 3m
Boundary conditions
  Infiltration from the top at the rate 0.05 [mol m-2 s-1]
A
B

## Slide 9: Model Setup
Simulation Domain
Process Kernel Tree
Model parameters
  numerical parameters
  physical parameters
Initial and Boundary conditions
Setting Forcing

## Slide 10: Jump to notebook

## Slide 11: Overland Flow
Diffusion Wave Model

## Slide 12: Diffusive wave model (DSW)
This model has been used to simulate overland flow in wetlands and open channels.
Describe shallow water movement across land surface:
  rainfall has exceeded the infiltration rate
  entire soil column becomes completely saturated and water exfiltrates at the surface

## Slide 13: Diffusive Wave Model of Overland Flow
Q - sources [mol m -2 s-1 ]
nmann- Manning coefficient [s m-1/3]
Zs - surface elevation [m-1]
ε - regularization [m]
Wasantha Lal (1998)
where the unknowns are the ponded depth of water hw [m], and the flux of surface water qs [mol m-1 s-1]

## Slide 14: Meshes for model design
Ω
Г丄
Г

## Slide 15: Overland Flow on a planar hillslope
Case1: no flow BC
Case2: critical depth BC
Case3: zero gradient BC
Case4: max depth BC

## Slide 16: Jump to notebook

## Slide 17: Integrated Hydrology
Coupled surface and subsurface flow

## Slide 18: Arcos Multiphysics Framework
Dynamic Data Manager
Dependency Graph
Process Kernel Tree
Coon et al. Env. Model. & Soft. 2016
The Arcos multiphysics framework, is a fully functional framework serving Amanzi and ATS, but may also be viewed as a reference implementation to explore interface designs, coupling strategies and outreach to the community.

## Slide 19: Model Coupling: Approach
Develop and test Process Kernels (PKs), such as, flow, transport, and energy in isolation.
Develop Multi-Process Couplers (MPCs) to create and test an integrated model.
MPCs fall in two categories:
  Strong: forms and solves a single system of equations (e.g., fully implicit)
  Weak: sequentially steps cycles through the process kernels (typical in flow and transport)
Users are able to express the coupled model at high-level in the input file using PK-trees.
PK-tree describing integrated hydrology.
The Arcos framework supports a flexible and phased approach to development and testing:

## Slide 20: Integrated Hydrology: Coupling Details
Combine matrices (and or Jacobians) of the two models together in a single system.
Use continuity of normal flux and pressure to create this fully coupled system.
  rewrite ponded depth as pressure
Appropriately match entities from one domain to the other, e.g., normal flux from a subsurface face is a source in that cell for surface flow.
Ensure conservation of mass
Schematic showing the locations on the mesh of the discrete unknowns in the subsurface flow (pressure: p - cells, 𝞴- faces ), q normal flux; and surface flow (ponded depth: h- cells, qs normal flux).
Coon E. T., et al., 2020, https://doi.org/10.1016/j.advwatres.2020.103701

## Slide 21: Model Setup
Simulation Domain
Process Kernel Tree
Model parameters
Initial and Boundary conditions
Setting Forcing

## Slide 22: Simulation Domain

## Slide 23: Process Kernel Tree
A single PK is the simplest PK-Tree you can have and doesn’t need a coupler, just the top-level cycle driver.
Schematic of the PK-tree for subsurface flow.
First, we introduced subsurface flow using Richards Equation:
Input file showing the “cycle driver” element with the PK-tree sublist for subsurface flow.

## Slide 24: Process Kernel Tree
A single PK is the simplest PK-Tree you can have and doesn’t need a coupler, just the top-level cycle driver.
Schematic of the PK-tree for overland flow.
Second, we introduced overland flow using a Diffusion Wave Equation:
Input file showing the “cycle driver” element with the PK-tree sublist for overland flow.

## Slide 25: Model Coupling (PK-Trees)
Schematic of the PK-tree for Integrated Hydrology (coupled overland and subsurface flow).
Finally, we couple surface and subsurface flow models
Input file showing the “cycle driver” element with the PK-tree sublist for coupled overland and subsurface flow (integrated hydrology).
to create the Integrated Hydrology model.

## Slide 26: Model Setup
Simulation Domain
Process Kernel Tree
Model parameters
Initial and Boundary conditions
Setting Forcing

## Slide 27
no flow
no flow
no flow
seepage head

## Slide 28: Jump to the notebook
Integrated hydrology:
2D hillslope transect
  explore model setup and run existing input file

## Slide 29
no flow
no flow
seepage head
lake
hydrostatic pressure

## Slide 30: Jump to the notebook
Integrated hydrology:
2D hillslope transect
  explore model setup and run existing input file

## Slide 31
no flow
no flow
seepage head
lake
hydrostatic pressure